## Slide 1: Control and Optimization of Smart Grid
Steven Low
Computing + Math Sciences
Electrical Engineering
March 2015
Cornell Ithaca
Notes: Caltech power system research:
Network architecture
June 2012: Caltech IST Advisory Board Meeting, Palo Alto (Mathieu Desbrun)
Oct 2012: GridWise Council Meeting (Paul, DeMartini, Ron Meltzer)
Dec 2012: Workshop on smart grid, University of Florida, Gainsville, FL (Sean Meyn)
Dec 2012: SCE Tech Advisory Board meeting, Westminster, CA
Dec 2012: Resnick Grid 2020 Seminar Panel, Caltech (Paul, DeMartini)
March 2013: Resnick Advisory Council, Caltech
April 2013: BCG, San Francisco, CA
May 21, 2013: Honeywell visit, Caltech (Rhonda Germany – Vice President, Chief Strategy & Marketing Officer, and team)
June 4, 2013: Electric Power Control Centers (EPCC) Workshop (Dejan Sobajic <dsobajic@gridengineering.com>)
June 25, 2013: FERC Technical Conference on Increasing Real-Time and Day-Ahead Market Efficiency through Improved Software (Richard O’Neill)
Branch Flow Model: relaxations, convexification, computation
May 24, 2012: Optimization and Control for Smart Grids, 32nd CNLS Annual Conference, Santa Fe, NM (Misha Chertkov)
June 11, 2012: Greenmetrics Workshop, London, UK (Adam Wierman)
June 26, 2012: FERC Conference, Washington D.C. (Dick O’Neil)
July 31, 2012: Energy Day, Chinese University of Hong Kong (Minghua Chen)
Aug 2, 2012: HK University of Science & Technology (Vince Lau, Roger)
Aug 3, 2012: Hong Kong University, EE Dept, HK (Victor Li)
Aug 6, 2012: Tsinghua University, Institute of Theoretical Computer Science, Beijing, China (Raymond Yeung)
Aug 17, 2012: Zhejiang University, EE Dept, Hang Zhou, China (Jiming Chen)
Aug 20, 2012: Shanghai Jiaotong University, EE Dept, Shanghai, China (Xinbing Wang)
Sept 5, 2012: U Texas A&M, Dept of ECE, Fishbowl Seminar Series (Srinivas Shakkottai)
Sept 2012: Swinburne University, Australia (Lachlan Andrew)
Nov 15, 2012: Distinguished Speaker, Northeast University, Boston MA (Edmund Yeh)
Equivalence of Branch Flow and Bus Injection Models
Oct 5, 2012: 50th Annual Allerton Conference (Dominguez-Garcia, Alejandro)
Exact relaxation for radial networks
Nov 6, 2012: IEEE SmartGridComm Conference (Tainan, Taiwan)
Jan 25, 2013: SUNY Buffalo, EE Dept (Dimitri Pados)
Feb 20, 2013: DIMACS workshop, Rutgers University, NJ (Dan Bienstock, SL)
March 20, 2013: UCLA SMERC Lecture (Rajit Gadh)
March 21, 2013: Systems and optimization aspects of smart grid challenges 2013, U Arizona, Tucson
March 28, 2013: Michigan, Ann Arbor (Ian Hiskens)
June 5, 2013: Electric Power Control Center (EPCC) Workshop (Dejan Sobajic, NYISO)
June 19, 2013: ACC Smart Grid Tutorial (Dennice Gayme, Ufuk Topcu)
July 4, 2013: 2nd International Workshop on Mathematical Issues in Information Sciences, Xi’an, China (Tom Luo)
August 25-30, 2013: IREP Symposium-Bulk Power System Dynamics and Control -IX (IREP), Rethymnon, Greece
Smart grid and OPF
Sept 26, 2013: Science & Technology Innovators Lecture Series, DTC, U of Minnesota, Minneapolis, MN (Giannakis)
November 29, 2013: University of Waterloo, Canadan (S. Keshav)
Feb 12, 2014: University of Washington, Seattle (Daniel Kerschen)
March 25-28, 2014: Short course, Zhejiang University [with Vincent Lau, HKUST] (Jiming Chen, Prof Zhang)
Tutorial: Convex relaxation of OPF
April 23, 2014: RTE-IBM workshop on “Semidefinite Programming for Optimal Power Flow Problems”, Dublin, Ireland (Patrick Panciatici, RTE)
June 19-23, 2014: Lehigh University, PA (Nader Motee)
August 20, 2014: PSCC invited session, Wroclaw, Poland (Patrick Panciatici)
Oct 15, 2014: LCCC Workshop on Dynamics and Control in Networks, Lund, Sweden (Anders Rantzer)
Oct 27, 2014: IEEE Trans on Control of Network Systems Symposium, Boston (Yannis Paschilidis)
High-level Smart Grid Research
Feb 2015: Caltech Lunch Bunch
Mar 16, 2015: Workshop: Information and Communication Systems and their application to vertical sectors (Fernando Paganini, Daniel Kofman)
March 18, 2015: Cornell NYCTech (Dan Huttenlocher)
March 20, 2015: Cornell Ithaca (Lang Tong)

## Slide 2: rsrg
theory
Internet: largest distributed nonlinear feedback control system
SISL
NetLab
prof steven low
2001
2000
Lee Center
2002
2003
2004
2005
2006
FAST TCP theory
IPAM Wkp
SC02 Demo
2007
WAN-in-Lab Testbed
Caltech FAST Project
control & optimization of networks
theory
experiment
deployment
testbed
Collaborators: Profs Doyle (Caltech), Newman (Caltech), Paganini (Uruguay), Tang (Cornell), Andrew (Swinburne), Chiang (Princeton);
CACR, CERN, Internet2, SLAC, Fermi Lab, StarLight, Cisco, Level(3)
testbed
experiment
deployment
Reverse engineering: TCP is real-time distributed algorithm over Internet to maximize utility
Forward engineering: Invention of FastTCP based on control theory & convex optimization
Internet2 LSR
SuperComputing BC
SC 2004
Scientists have used FastTCP to break world records on data transfer between 2002 – 2006
FAST is commercialized by FastSoft; it accelerates world’s 2nd largest CDN and Fortune 100 companies
FastTCP
TCP
Internet
FAST in a box
WAN-in-Lab : one-of-a-kind wind- tunnel in academic networking, with 2,400km of fiber, optical switches, routers, servers, accelerators
with FAST
without FAST
eq 1
eq 2
eq 3
Lee Center

## Slide 3: rsrg
SISL
NetLab
prof steven low
2001
2000
Lee Center
2002
2003
2004
2005
2006
FAST TCP theory
IPAM Wkp
SC02 Demo
2007
WAN-in-Lab Testbed
Caltech FAST Project
Lee Center
2012
2014
accelerating largest social networks, studios,
and other Fortune 100 companies
“FAST TCP is accelerating >1TB
of internet traffic every second !”

## Slide 4: Vision (20+ yrs)
Global energy demand will continue to grow
Traditional supply is unsustainable
There is more renewable energy than the world ever needs
  Someone will figure out how to capture and store it
There will be connected intelligence everywhere
  Cost of computing, storage, communication and manufacturing will continue to drop
Power system will transform into the largest and most complex Internet of Things
  Generation, transmission, distribution, consumption, storage

## Slide 5: Mission
To develop technologies that will enable and guide the historic transformation of our power system
  Generation, transmission, distribution, consumption, storage
  Devices, systems, theory, algorithms
  Control, optimization, stochastics, data, economics

## Slide 6: Outline
Overview & challenges
Optimal power flow
Frequency regulation
Applications

## Slide 7: Watershed moment
Bell: telephone
1876
Tesla: multi-phase AC
1888
Both started as natural monopolies
Both provided a single commodity
Both grew rapidly through two WWs
1980-90s
1980-90s
Deregulation
started
Deregulation
started
Power network will undergo similar architectural
transformation that phone network went through
in the last two decades
IoT
1969:
DARPAnet
Convergence
to Internet

## Slide 8: Watershed moment
Industries will be destroyed & created
  AT&T, MCI, McCaw Cellular, Qualcom
  Google, Facebook, Twitter, Amazon, eBay, Netflix
Infrastructure will be reshaped
  Centralized intelligence, vertically optimized
  Distributed intelligence, layered architecture
What will drive power network transformation ?

## Slide 9: Four drivers
Advances in power electronics
Deployment of sensing, control, comm
Proliferation of renewables
Electrification of transportation
challenges
enablers

## Slide 10: Uncertainty
High Levels of Wind and Solar PV Will Present an Operating Challenge!
Source: Rosa Yang, EPRI

## Slide 11
Source: Leon Roose, University of Hawaii
Development & demo of smart grid inverters for high-penetration PV applications
Voltage violations are quite frequent

## Slide 12
network of
billions of active distributed energy resources (DERs)
DER: PV, wind tb, EV, storage, smart appliances
Solar power over land:
> 20x world energy demand

## Slide 13
Risk: active DERs introduce rapid random
fluctuations in supply, demand, power quality
increasing risk of blackouts
Opportunity: active DERs enables realtime
dynamic network-wide feedback control,
improving robustness, security, efficiency
Caltech research: distributed control of networked DERs
Foundational theory, practical algorithms, concrete
applications
Integrate engineering and economics
Active collaboration with industry

## Slide 14: Active DERs: implications
Current control paradigm works well today
  Centralized, open-loop, human-in-loop, worst-case preventive
  Low uncertainty, few active assets to control
  Schedule supplies to match loads
Future needs
  Closing the loop, e.g. real-time DR, volt/var
  Fast computation to cope with rapid, random, large fluctuations in supply, demand, voltage, freq
  Simple algorithms to scale to large networks of active DER
  Market mechanisms to incentivize

## Slide 15: Need for distributed control
Example: Southern California Edison
  4-5 million customers
SCE Rossi feeder circuit
  #houses: 1,407; #commercial/industrial: 131
  #transformers: 422
  #lines: 2,064 (multiphase, inc. transfomers)
  peak load: 3 – 6 MW
  #optimization variables: 50,000
SCE has 4,500 feeders
  ~100M variables
United States
  131M customers, 300K miles of transmission & distr lines, 3,100 utilities

## Slide 16: Key challenges
Nonconvexity
  Convex relaxations
Large scale
  Distributed algorithms
Uncertainty
  Risk-limiting approach
Multiple timescales
  Decomposition
Ian Hiskens, Michigan

## Slide 17: Our research
sec
min
hour
day
year
freq control
volt/var
EV charging
storage
demand
response
control
and
optimization
economics
and
regulations
DER
adoption
market
power
optimal power flow (OPF)
Infrastructure inv.

## Slide 18: Outline
Overview & challenges
Optimal power flow (OPF)
  problem formulation
  semidefinite relaxations
  exact relaxation
Frequency regulation
Applications

## Slide 19: Optimal power flow (OPF)
OPF is solved routinely for
  network control & optimization decisions
  market operations & pricing
  at timescales of mins, hours, days, …
Non-convex and hard to solve
  Huge literature since Carpentier 1962
  Common practice: DC power flow (LP)
  Also: Newton-Raphson, interior point, …

## Slide 20: Optimal power flow (OPF)
OPF underlies many applications
  Unit commitment, economic dispatch
  State estimation
  Contingency analysis
  Feeder reconfiguration, topology control
  Placement and sizing of capacitors, storage
  Volt/var control in distribution systems
  Demand response, load control
  Electric vehicle charging
  Market power analysis
  …

## Slide 21: Nonconvexity of OPF
Semidefinite relaxations of power flows
  Physical systems are nonconvex …
  … but have hidden convexity that should be exploited
Convexity is important for OPF
  Foundation of LMP, critical for efficient market theory
  Required to guarantee global optimality
  Required for real-time computation at scale

## Slide 23: Bus injection model
i
j
k
admittance matrix:
graph G: undirected
Y specifies topology of G and
impedances z on lines

## Slide 24: Bus injection model
Power flow problem:
Given find
In terms of :
isolated solutions

## Slide 25: OPF: bus injection model
power flow equation
gen cost,
power loss

## Slide 26: OPF: bus injection model
power flow equation
gen cost,
power loss

## Slide 27: OPF: bus injection model
nonconvex QCQP
(quad constrained quad program)

## Slide 28: Other features
Security constraint OPF
  Solve for operating points after each single contingency (N-1 security)
  N sets of variables and constraints, one for each contingency
Unit commitment
  Discrete variables
Stochastic OPF
  Chance constraints Pr(bad event) <
Other constraints
  Line flow, line loss, stability limit, …
… OPF in practice is a lot harder

## Slide 29: Semidefinite relaxations of OPF
relaxation | model | first proposed | first analyzed
SOCP | BIM | Jabr 2006 TPS | 
SDP | BIM | Bai et al 2008 EPES | Lavaei, Low 2012 TPS Bose et al 2011, 2015 Zhang, Tse 2011, 2013 Sojoudi, Lavaei 2012
Chordal | BIM | Bai, Wei 2011 EPES Jabr 2012 TPS | Molzahn et al 2013 TPS Bose et al 2014 TAC
SOCP | BFM | Farivar et al 2011 SGC Farivar, Low 2013 TPS | Farivar et al 2011 SGC Farivar, Low 2013 TPS Gan et al 2012, 2014
Chordal unbalanced | BFM | Gan, Low 2014 PSCC | Gan, Low 2014 PSCC
Tutorial with extensive refs:
Low. Convex relaxation of OPF (I, II), IEEE Trans Control of Network Systems, 2014

## Slide 30: Basic idea
Approach
  Three equivalent characterizations of V
  Each suggests a lift and relaxation
What is the relation among different relaxations ?
When will a relaxation be exact ?

## Slide 31: Feasible set & SDP
Equivalent problem:
convex in W
except this constraint
quadratic in V
linear in W

## Slide 32: Equivalent feasible sets
QCQP: n variables
SDP: n2 vars !

## Slide 33: Equivalent feasible sets

## Slide 34: Equivalent feasible sets

## Slide 35: Equivalent feasible sets

## Slide 36: Equivalent feasible sets

## Slide 37: Cycle condition
cycle
cond
local
global

## Slide 38: Equivalent feasible sets
Bose, Low, Chandy Allerton 2012
Bose, Low, Teeraratkul, Hassibi TAC2014
Theorem:

## Slide 39: Equivalent feasible sets
Theorem:
Given there is
unique completion and unique
Can minimize cost over any of these sets, but …

## Slide 40: Equivalent feasible sets

## Slide 41: Relaxations
Theorem
  Radial G :
  Mesh G :
Bose, Low, Chandy Allerton 2012
Bose, Low, Teeraratkul, Hassibi TAC2014

## Slide 42: Relaxations
Theorem
  Radial G :
  Mesh G :
For radial networks: always solve SOCP !

## Slide 43: Recap: semidef relaxations
G

## Slide 44: Examples
power flow
solution X
SDP Y
SOCP Y
Real Power
Reactive Power
Relaxation is exact if X and Y have same Pareto front
SOCP is faster but coarser than SDP
Bose, Low, Teeraratkul, Hassibi TAC 2014

## Slide 45: Without PS: SDP vs SOCP
SDP not
scalable
SOCP
inexact
SDP
SOCP
SOCP
SDP

## Slide 46: Examples
SDP not
scalable
SOCP
inexact
SDP/ch
SOCP
SOCP
SDP
chordal

## Slide 47: SOCP more efficient than SDP
Relaxations are exact in all cases
IEEE networks: IEEE 13, 34, 37, 123 buses (0% DG)
SCE networks 47 buses (57% PV), 56 buses (130% PV)
Single phase; SOCP using BFM
Matlab 7.9.0.529 (64-bit) with CVX 1.21 on Mac OS X 10.7.5 with 2.66GHz Intel Core 2 Due CPU and 4GB 1067MHz DDR3 memory

## Slide 48
OPF-socp
OPF solution
Recover V*
cycle
condition
Y
rank-1
OPF-ch
OPF-sdp
Y
Y, mesh
2x2 rank-1
Y
radial
OPF-socp
cycle
condition
Y
equality
Y
radial
Y, mesh

## Slide 49
OPF-socp
OPF solution
Recover V*
cycle
condition
Y
rank-1
OPF-ch
OPF-sdp
Y
Y, mesh
2x2 rank-1
Y
radial
OPF-socp
cycle
condition
Y
equality
Y
radial
Y, mesh

## Slide 50
OPF-socp
OPF solution
Recover V*
cycle
condition
Y
rank-1
OPF-ch
OPF-sdp
Y
Y, mesh
2x2 rank-1
Y
radial
OPF-socp
cycle
condition
Y
equality
Y
radial
Y, mesh
open problem
open problem

## Slide 51
What is the relation among relaxations ?
When will a relaxation be exact ?

## Slide 52: Summary of sufficient conds
necessary condition for exact relaxation:
Louca, Seiler, Bitar 2014

## Slide 53: 1. QCQP over tree
graph of QCQP
QCQP
QCQP over tree

## Slide 54: 1. Linear separability
Key condition
QCQP
Theorem
SOCP relaxation is exact for
QCQP over tree
Bose et al 2012, 2014
Sojoudi, Lavaei 2013

## Slide 55: Implication on OPF
Not both lower & upper bounds on real & reactive powers at both ends
of a line can be finite

## Slide 56: 2. Voltage upper bounds
geometric insight

## Slide 57: 2. Voltage upper bounds
when there is no voltage constraint
feasible set : 2 intersection pts
relaxation: line segment
exact relaxation: c is optimal
… as long as cost increasing in

## Slide 58: 2. Voltage upper bounds
voltage lower bound (upper bound on l) does not affect relaxation

## Slide 59: 2. Voltage upper bounds
Gan, Li, Topcu, Low TAC2014
Theorem
SOCP relaxation is exact for
radial networks
OPF:
SOCP:
Key conditions:
  Jacobian condition
voltages if network were lossless
if upward current were reduced
then all subsequent powers dec

## Slide 60: 2. Voltage upper bounds
Key conditions:
  Jacobian condition
Gan, Li, Topcu, Low TAC2014
Theorem
SOCP relaxation is exact for
radial networks
OPF:
SOCP:
satisfied with large margin in
IEEE circuits and SCE circuits

## Slide 61: OPF: extensions
exactness
distributed
OPF
Kim, Baldick 1997
Dall’Anese et al 2012
Lam et al 2012
Kraning et al 2013
Devane, Lestas 2013
Sun et al 2013
Li et al 2013
Peng, Low 2014
moment/SoS,
based
relaxation
Molzahn, Hiskens 2014
Josz et al 2014
Ghaddar et al 2014
multiphase
unbalanced
Dall’Anese et al 2012
Gan, Low 2014
semidefinite relaxations
applications
B&B,
rank min,
QC relaxation,
Phan 2012
Gopalakrishnan 2012
Louca et al 2013
Hijazi et al 2013
ext refs in Low
TCNS 2014
Louca et al 2014

## Slide 62: Outline
Overview & challenges
Optimal power flow (OPF)
Frequency regulation
  load-side participation
  algorithm design and stability
Applications

## Slide 63: Motivation
2011 Southwest blackout
(1 min)
  All buses synchronized to same nominal frequency (US: 60 Hz; Europe: 50 Hz)
  Supply-demand imbalance  frequency fluctuation

## Slide 64: Motivation
Imagine when we have 33%+ renewable generation …
(1 min)
(10 min)

## Slide 65: Frequency control
sec
min
5 min
60 min
primary
freq control
secondary freq control
economic
dispatch
Traditionally done on generator-side
  primary: rebalance power, resynchronize freq
  secondary: restore nominal freq & inter-area flows
  tertiary (EC): maximize economic efficiency

## Slide 66: Why load-side participation
sec
min
5 min
60 min
primary
freq control
secondary freq control
economic
dispatch
Ubiquitous continuous load-side control can supplement generator-side control
  faster (no/low inertia)
  no extra waste or emission
  more reliable (large #)
  better localize disturbances
  reducing generator-side control capacity

## Slide 67: What is the potential
US:
operating reserve: 13% of peak
total GFA capacity: 18%
Lu & Hammerstrom (2006), PNNL
Residential load accounts
for ~1/3 of peak demand
61% residential appliances
are Grid Friendly

## Slide 68
Callaway, Hiskens (2011)
Callaway (2009)
Can household Grid Friendly
appliances follow its own PV
production?
Dynamically adjust
thermostat setpoint
60,000 AC
avg demand ~ 140 MW
wind var: +- 40MW
temp var: 0.15 degC

## Slide 69: How
How to design load-side frequency control ?
How does it interact with generator-side control ?

## Slide 70: Literature: load-side control
Original idea
  Schweppe et al 1979, 1980
Small scale trials around the world
  D.Hammerstrom et al 2007, UK Market Transform Programme 2008
Numerical studies
  Trudnowski et al 2006, Lu and Hammerstrom 2006, Short et al 2007, Donnelly et al 2010, Brooks et al 2010, Callaway and I. A. Hiskens, 2011, Molina-Garcia et al 2011
Analytical studies
  Zhao et al (2012/2014), Mallada et al (2014), Zhao and Low (2014)
  Simpson-Porco et al 2013, You and Chen 2014, Zhang and Papachristodoulou (2014), Zhao, et al (2014)

## Slide 71: Our work
basic design
approach:
primary
linear
secondary
nonlinear
Mallada et al 2014 Allerton
Zhao et al 2015 CISS
Zhao et al 2014 TAC
w/ gen control
secondary
nonlinear
Zhao, Low 2014 CDC

## Slide 72: Network model
generation
loads:
controllable + uncontrollable
i : region/control area/balancing authority
branch power

## Slide 73: Dynamic model
generator bus: real power injection

## Slide 74: Dynamic model
generator buses:

## Slide 75: Dynamic model
load bus: controllable load
how to design controller di(t) ?
Proposed approach
  formalize control goals as OLC
  derive distributed control as primal-dual alg

## Slide 76: Load-side controller design
Control goals
  Rebalance power
  Stabilize frequency
  Restore nominal frequency
  Restore scheduled inter-area flows
Zhao, Topcu, Li, Low
TAC 2014
Mallada, Zhao, Low
Allerton, 2014

## Slide 77: Optimal load control (OLC)
in steady state: virtual = real flows
key idea: “virtual flows”
demand = supply

## Slide 78: Optimal load control (OLC)
restore nominal freq
in steady state: virtual = real flows
demand = supply

## Slide 79: Optimal load control (OLC)
restore nominal freq
in steady state: virtual = real flows
restore inter-area flow
respect line limit
demand = supply

## Slide 80: Distributed load control
load control:
local frequency deviation
measured locally at load
virtual frequency
computed locally based on neighborhood comm
network dynamics + active load control
= first-order primal-dual algorithm for OLC

## Slide 81: Distributed control architecture
physical
cyber

## Slide 82: Load-side control works
Theorem
Every closed-loop equilibrium solves OLC and its dual
Suppose
Any closed-loop equilibrium is (locally) asymptotically stable provided

## Slide 83: Simulations
Dynamic simulation of IEEE 39-bus system
Power System Toolbox (RPI)
Detailed generation model
Exciter model, power system
stabilizer model
Nonzero resistance lines

## Slide 84: Primary control
Can replacing gen-side control
with load-side control
Load-side participation improves
transient and steady state
PSS 39-bus, same control capacity
Primary frqueny control
PSS 14-bus, same control capacity
Secondary frequency control

## Slide 85: Recap
Forward-engineering design facilitates
  explicit control goals
  distributed algorithms
  stability analysis
Load-side frequency regulation
  essential as renewable replaces thermal gen
  improves generator-side control

## Slide 86: Outline
Overview
Optimal power flow (OPF)
Frequency regulation
  problem formulation
  semidefinite relaxations
  exact relaxation
Applications

## Slide 87: OPF research
Theoretical foundation
semidefinite relaxations of OPF
2012
2013
2014
2016
Algorithm design
unbalanced OPF, distributed OPF
Implementation & T2M
IoT gateway, testbed, field test
2015

## Slide 88
IoT gateway prototype
sense
control
communicate
compute
power
voltage
frequency
EV charger
thermostat
inverters
IoT gateway
WiFi/4G
cloud
OPF
freq control
George Lee

## Slide 89: Testbed

## Slide 90: Field test
EV charging
HVAC control
app
sense
control
comm
compute
George Lee

## Slide 91: Tech-to-market
IoT has been growing
at unprecedented rate
Energy is the largest
application for IoT

## Slide 92: Tech-to-market
SG IT software is
already a multi-B
market

## Slide 93
Risk: active DERs introduce rapid random
fluctuations in supply, demand, power quality
increasing risk of blackouts
Opportunity: active DERs enables realtime
dynamic network-wide feedback control,
improving robustness, security, efficiency
Caltech research: distributed control of networked DERs
Foundational theory, practical algorithms, concrete
applications
Integrate engineering and economics
Active collaboration with industry