## Slide 1: Design and Stability of Load-side Frequency Control
Changhong Zhao*
Enrique Mallada*
Steven Low
EE, CMS, Caltech
July 2015
Lina Li
Harvard
Ufuk Topcu
U Penn
Notes: May 2012: Santa Fe Institute Workshop on Smart Grid, Santa Fe, NM
July 2012: Network Science Workshop, Chinese University of Hong Kong, HK (Raymond Yeung)
Sept 2012: Melbourne University, EEE Department (Pascal van Hentenryck)
February 13, 2013: ITA Workshop, San Diego
May 20, 2013: IEEE Workshop on Modeling and Simulation of Cyber-Physical Energy Systems, Berkeley, CA (Peter Palensky, Edward A. Lee)
Oct 31, 2013: Google, Mountain View, CA (Arun Mazumdar)
Nov 5, 2013: Asilomar Conference, invited session on Power Networks (Edmund Yeh)
Nov 15, 2013: NSF Workshop on Smart Grid, Washington DC (Giannakis, Sairaj, SL)
Dec 2, 2013: UCLA EE (Mani Srivastava)
Dec 5, 2013: Keynote, GlobalSIP (Global Conf on Signal & Info Processing) Symposium on Signal Processing in Smart Grid (Shalinee Kishore, Lalitha Sankar)
Jan 16, 2014: Stanford Smart Grid seminar (Ram Rajagopal, Baosen Zhang)
Feb 4, 2014: 9th Annual CARNEGIE MELLON CONFERENCE ON THE ELECTRICITY INDUSTRY, (Marija Ilic, Krishnan Kant)
May 22, 2014: UC Berkeley (Kameshwar)
Oct 3, 2014: ASU (Junshan Zhang)
Nov 3, 2014: Asilomar Conference, invited session on Smart Grid: learning and optimization, Pacific Grove, CA
Nov 10, 2014: EE Control Group, Berkeley (Claire Tomlin)
Jan 16, 2015, Grid Science Winter School and Conference (Scott Backhaus, Misha Chertkov)
June 9, 2015: Advanced Mathematical Methods For Energy Systems: from Theory to Practice, Moscow, Russia (Janusz Bialek, Skoltech)
July 7, 2015, Tsinghua power systems group (Prof Song Yonghua)
July 21, 2015: Hong Kong University, EEE (David Hill, Victor Li)

## Slide 2: Motivation
2011 Southwest blackout
(1 min)
  All buses synchronized to same nominal frequency (US: 60 Hz; Europe/China: 50 Hz)
  Supply-demand imbalance  frequency fluctuation

## Slide 3: Motivation
Imagine when we have 50%+ renewable generation …
(1 min)
(10 min)

## Slide 4: Why load-side participation
sec
min
5 min
60 min
primary
freq control
secondary freq control
economic
dispatch
Ubiquitous continuous load-side control can supplement generator-side control
  faster (no/low inertia)
  no extra waste or emission
  more reliable (large #)
  better localize disturbances
  reducing generator-side control capacity

## Slide 5: What is the potential
US:
operating reserve: 13% of peak
total GFA capacity: 18%
Lu & Hammerstrom (2006), PNNL
Residential load accounts
for ~1/3 of peak demand
61% residential appliances
are Grid Friendly

## Slide 6: How
How to design load-side frequency control ?
How does it interact with generator-side control ?

## Slide 7: Literature: load-side control
Original idea & early analytical work
  Schweppe et al 1980; Bergin, Hill, Qu, Dorsey, Wang, Varaiya …
Small scale trials around the world
  D.Hammerstrom et al 2007, UK Market Transform Programme 2008
Early simulation studies
  Trudnowski et al 2006, Lu and Hammerstrom 2006, Short et al 2007, Donnelly et al 2010, Brooks et al 2010, Callaway and I. A. Hiskens, 2011, Molina-Garcia et al 2011
Analytical work – load-side control
  Zhao et al (2012/2014), Mallada and Low (2014), Mallada et al (2014), Zhao and Low (2014), Zhao et al (2015)
  Simpson-Porco et al 2013, You and Chen 2014, Zhang and Papachristodoulou (2014), Ma et al (2014), Zhao, et al (2014),
Recent analysis – generator-side/microgrid control:
  Andreasson et al (2013), Zhang and Papachristodoulou (2013), Li et al (2014), Burger et al (2014), You and Chen (2014), Simpson-Porco et al (2013), Hill et al (2014), Dorfler et al (2014)

## Slide 8: Outline
Network model
Load-side frequency control
Simulations
Details
Main references:
Zhao, Topcu, Li, Low, TAC 2014
Mallada, Zhao, Low, Allerton 2014
Zhao, Low, CDC 2014, Zhao et al CISS 2015

## Slide 9: Network model
generation
loads:
controllable + freq-sensitive
i : region/control area/balancing authority
branch power
Will include generator-side
control later

## Slide 10: Network model
Generator bus: Mi > 0
Load bus: Mi = 0
Damping/uncontr loads:
Controllable loads:

## Slide 11: Network model
swing dynamics
all variables are deviations
from nominal
extends to nonlinear power flow

## Slide 12: Frequency control
Suppose the system is in steady state
Then: disturbance in gen/load …

## Slide 13: Frequency control
current
approach
load-side
control

## Slide 14: Frequency control
Given: disturbance in gens/loads
Current: adapt remaining generators
  re-balance power
  restore nominal freq and inter-area flows (zero ACE)
Our goal: adapt controllable loads
  re-balance power
  restore nominal freq and inter-area flows
  … while minimizing disutility of load control

## Slide 15: Outline
Network model
Load-side frequency control
Simulations
Details
Main references:
Zhao, Topcu, Li, Low, TAC 2014
Mallada, Zhao, Low, Allerton 2014
Zhao, Low, CDC 2014, Zhao et al CISS 2015

## Slide 16: Load-side controller design
Control goals (while min disutility)
  Rebalance power & stabilize frequency
  Restore nominal frequency
  Restore scheduled inter-area flows
  Respect line limits
Zhao, Topcu, Li, Low
TAC 2014
Mallada, Zhao, Low
Allerton, 2014

## Slide 17: Load-side controller design
Control goals (while min disutility)
  Rebalance power & stabilize frequency
  Restore nominal frequency
  Restore scheduled inter-area flows
  Respect line limits
Zhao, Topcu, Li, Low
TAC 2014
Mallada, Zhao, Low
Allerton, 2014

## Slide 18: Load-side controller design
Design control law
whose equilibrium
solves:
power balance
inter-area flows
line limits
Control goals (while min disutility)
  Rebalance power & stabilize frequency
  Restore nominal frequency
  Restore scheduled inter-area flows
  Respect line limits
load disutility
freq will emerge as
Lagrange multiplier
for power imbalance

## Slide 19: Load-side controller design
Design control (G, F) s.t. closed-loop system
  is stable
  has equilibrium that is optimal
power network
load control

## Slide 20: Load-side controller design
Idea: exploit system dynamic as part of primal-dual algorithm for modified opt
  Distributed algorithm
  Stability analysis
  Control goals in equilibrium
power network
load control

## Slide 21: Summary: control architecture
Primary load-side frequency control
completely decentralized
Theorem: stable dynamic, optimal equilibrium
Zhao, Topcu, Li, Low. TAC 2014
physical network

## Slide 22: Summary: control architecture
Mallada, Zhao, Low. Allerton 2014
Secondary load-side frequency control
communication with neighbors
Theorem: stable dynamic, optimal equilibrium
physical network
cyber network

## Slide 23: Summary: control architecture
With generator-side control, nonlinear power flow
load-side improves both transient & eq
Theorem: stable dynamic, optimal equilibrium
Zhao, Mallada, Low. CISS 2015
physical network
cyber network

## Slide 24
example:
secondary control

## Slide 25: Recall: design approach
Idea: exploit system dynamic as part of primal-dual algorithm for modified opt
  closed-loop system is stable
  its equilibria are optimal
power network
load control

## Slide 26: OLC for secondary control
restore nominal freq
demand = supply

## Slide 27: OLC for secondary control
key idea: “virtual flows”
demand = supply
in steady state:
virtual flow = real flows
restore nominal freq

## Slide 28: OLC for secondary control
restore nominal freq
in steady state:
virtual flow = real flows
restore inter-area flow
respect line limit
demand = supply

## Slide 29: Control architecture

## Slide 30: Secondary frequency control
load control:
computation & communication:
primal var:
dual vars:

## Slide 31: Secondary control works
Theorem
starting from any initial point, system
trajectory converges s. t.
  is unique optimal of OLC
  nominal frequency is restored
  inter-area flows are restored
  line limits are respected

## Slide 32: Recap: key ideas
Design optimal load control (OLC) problem
  Objective function, constraints
Derive control law as primal-dual algorithms
  Lyapunov stability
  Achieve original control goals in equilibrium
Distributed algorithms
primary control:
secondary control:

## Slide 33: Recap: key ideas
Design optimal load control (OLC) problem
  Objective function, constraints
Derive control law as primal-dual algorithms
  Lyapunov stability
  Achieve original control goals in equilibrium
Distributed algorithms
Virtual flows
  Enforce desired properties on line flows
in steady state: virtual flow = real flows

## Slide 34: Outline
Network model
Load-side frequency control
Simulations
Details
Main references:
Zhao, Topcu, Li, Low, TAC 2014
Mallada, Zhao, Low, Allerton 2014
Zhao, Low, CDC 2014, Zhao et al CISS 2015

## Slide 35: Simulations
Dynamic simulation of IEEE 39-bus system
Power System Toolbox (RPI)
Detailed generation model
Exciter model, power system
stabilizer model
Nonzero resistance lines

## Slide 36: Primary control

## Slide 37: Secondary control
swing dynamics
with OLC
area 1

## Slide 38: Secondary control
no line limits
with line limits
Total inter-area flow is
the same in both cases
line limit
line limit

## Slide 39: Conclusion
Forward-engineering design facilitates
  explicit control goals
  distributed algorithms
  stability analysis
Load-side frequency regulation
  primary & secondary control works
  helps generator-side control

## Slide 40: Outline
Network model
Load-side frequency control
Simulations
Details
Main references:
Zhao, Topcu, Li, Low, TAC 2014
Mallada, Zhao, Low, Allerton 2014
Zhao, Low, CDC 2014, Zhao et al CISS 2015

## Slide 41
more details
(backup)

## Slide 42: Recall: design approach
Idea: exploit system dynamic as part of primal-dual algorithm for modified opt
  closed-loop system is stable
  its equilibria are optimal
power network
load control

## Slide 43: Outline
Load-side frequency control
  Primary control
  Secondary control
  Interaction with generator-side control
Zhao et al SGC2012, Zhao et al TAC2014

## Slide 44: Optimal load control (OLC)
demand = supply
disturbances
controllable
loads

## Slide 45: system dynamics + load control = primal dual alg
swing dynamics
load control
active control
implicit

## Slide 46: Control architecture

## Slide 47: Load-side primary control works
Theorem
Starting from any
system trajectory
converges to
  is unique optimal of OLC
  is unique optimal for dual
completely decentralized
frequency deviations contain right info for local decisions that are globally optimal

## Slide 48: Recap: control goals
  Rebalance power
  Stabilize frequencies
  Restore nominal frequency
  Restore scheduled inter-area flows
  Respect line limits
Yes
Yes
No
No
No

## Slide 49: Outline
Load-side frequency control
  Primary control
  Secondary control
  Interaction with generator-side control
Mallada, Low, IFAC 2014
Mallada et al, Allerton 2014

## Slide 50: OLC for secondary control
restore nominal freq
demand = supply

## Slide 51: OLC for secondary control
key idea: “virtual flows”
demand = supply
in steady state:
virtual flow = real flows
restore nominal freq

## Slide 52: OLC for secondary control
restore nominal freq
in steady state:
virtual flow = real flows
restore inter-area flow
respect line limit
demand = supply

## Slide 53: Recall: primary control
swing dynamics:
load control:
active
control
implicit

## Slide 54: Control architecture
physical network
cyber network

## Slide 55: Secondary frequency control
load control:
computation & communication:
primal var:
dual vars:

## Slide 56: Secondary control works
Theorem
starting from any initial point, system
trajectory converges s. t.
  is unique optimal of OLC
  nominal frequency is restored
  inter-area flows are restored
  line limits are respected

## Slide 57: Recap: key ideas
Design optimal load control (OLC) problem
  Objective function, constraints
Derive control law as primal-dual algorithms
  Lyapunov stability
  Achieve original control goals in equilibrium
Distributed algorithms
primary control:
secondary control:

## Slide 58: Recap: key ideas
Design optimal load control (OLC) problem
  Objective function, constraints
Derive control law as primal-dual algorithms
  Lyapunov stability
  Achieve original control goals in equilibrium
Distributed algorithms
Virtual flows
  Enforce desired properties on line flows
in steady state: virtual flow = real flows

## Slide 59: Recap: control goals
  Rebalance power
  Resynchronize/stabilize frequency
  Restore nominal frequency
  Restore scheduled inter-area flows
  Respect line limits
Yes
Yes
Secondary control restores nominal
frequency but requires local communication
Yes
Yes
Mallada, et al Allerton2014
Zhao, et al TAC2014
Yes

## Slide 60: Outline
Load-side frequency control
  Primary control
  Secondary control
  Interaction with generator-side control
Zhao and Low, CDC2014
Zhao, Mallada, Low, CISS 2015

## Slide 61: Generator-side control
Recall model: linearized PF, no generator control
New model: nonlinear PF, with generator control

## Slide 62: Generator-side control
generator bus: real power injection
load bus: controllable load
New model: nonlinear PF, with generator control

## Slide 63: Generator-side control
New model: nonlinear PF, with generator control
generator buses:

## Slide 64: Load-side control
physical network
cyber network

## Slide 65: Load-side primary control works
Theorem
Every closed-loop equilibrium solves OLC and its dual
Suppose
Any closed-loop equilibrium is (locally) asymptotically stable provided