## Slide 1: Optimal Power Flow: online algorithm, fast dynamics
Steven Low
August 2016
Notes: May 2012: Santa Fe Institute Workshop on Smart Grid, Santa Fe, NM
July 2012: Network Science Workshop, Chinese University of Hong Kong, HK (Raymond Yeung)
Sept 2012: Melbourne University, EEE Department (Pascal van Hentenryck)
February 13, 2013: ITA Workshop, San Diego
May 20, 2013: IEEE Workshop on Modeling and Simulation of Cyber-Physical Energy Systems, Berkeley, CA (Peter Palensky, Edward A. Lee)
Oct 31, 2013: Google, Mountain View, CA (Arun Mazumdar)
Nov 5, 2013: Asilomar Conference, invited session on Power Networks (Edmund Yeh)
Nov 15, 2013: NSF Workshop on Smart Grid, Washington DC (Giannakis, Sairaj, SL)
Dec 2, 2013: UCLA EE (Mani Srivastava)
Dec 5, 2013: Keynote, GlobalSIP (Global Conf on Signal & Info Processing) Symposium on Signal Processing in Smart Grid (Shalinee Kishore, Lalitha Sankar)
Jan 16, 2014: Stanford Smart Grid seminar (Ram Rajagopal, Baosen Zhang)
Feb 4, 2014: 9th Annual CARNEGIE MELLON CONFERENCE ON THE ELECTRICITY INDUSTRY, (Marija Ilic, Krishnan Kant)
May 22, 2014: UC Berkeley (Kameshwar)
Oct 3, 2014: ASU (Junshan Zhang)
Nov 3, 2014: Asilomar Conference, invited session on Smart Grid: learning and optimization, Pacific Grove, CA
Nov 10, 2014: EE Control Group, Berkeley (Claire Tomlin)
Jan 16, 2015, Grid Science Winter School and Conference (Scott Backhaus, Misha Chertkov)
June 9, 2015: Advanced Mathematical Methods For Energy Systems: from Theory to Practice, Moscow, Russia (Janusz Bialek, Skoltech)
July 7, 2015, Tsinghua power systems group (Prof Song Yonghua)
July 21, 2015: Hong Kong University, EEE (David Hill, Victor Li)
Online algorithms for power systems
============================
Jan 14, 2016: IPAM Workshop on Optimization and Equilibrium of Energy Economics, UCLA, CA (Mike Ferris)
Jan 28, 2016: ESIF Workshop on Frontiers in Distributed Optimization and Control of Sustainable Power Systems, NREL, Golden, CO (Emiliano Dall’Anese, Brian Johnson)
Feb 8, 2016: PNNL (Jakob Stoustrup)
Feb 10, 2016: Georgia Tech, School of Industrial & Systems Engineering (Andy Sun)
March 10, 2016: Caltech CMI Faculty talk (Michelle Effros)
March 17, 2016: CISS Plenary talk, Princeton, NJ (Mung Chiang)
April 10, 2016: Tsinghua Electrical Engineering Dept (Profs Liu and Mei)
April 2016: Zhejiang University, EE (Prof Song Yonghua)
May 19, 2016: Information Modeling and Control of Complex Systems Workshop (Ohio State University, Ness Shroff)
June 16, 2016: ETH, Power Systems Lab (Goran Andersson)
June 26, 2016: Keynote, Conf on Uncertainty in Artificial Intelligence
OPF: relaxations, online algorithms, fast dynamics
=========================================
June 30, 2016: Simons Institute Workshop on Real-time Decision Making (Dick Karp)
July 14, 2016: GE Grid Solutions Monthly Tech Talk, Redmond, WA (Kwok Cheung)
August 26, 2016: EEE Department, University of Melbourne (Rob Evans)
Sept 6, 2016: EECS, University of Michigan (Johanna Mathieu)
Sept 23, 2016: EE, Harvard University (Lina Li)

## Slide 2
Li (Harvard)
Mallada (JHU)
Topcu (Austin)
Zhao (NREL)
Dynamics
Bose (UIUC)
Chandy
Farivar
Gan (FB)
Lavaei (UCB)
Gan (FB)
Online OPF
Dvijotham (PNNL)
Tang
Bialek (Skoltech)
OPF
relaxation

## Slide 4
network of
billions of active distributed energy resources (DERs)
DER: PV, wind tb, EV, storage, smart bldg / appl
Solar power over land:
> 20x world energy demand

## Slide 5: Multiple timescales
System dynamics and controls at different timescales
require different models
power flow models
(algebraic equations)
dynamic models
(ODEs)

## Slide 6: Optimal power flow (OPF)
OPF is solved routinely for
  network control & optimization decisions
  market operations & pricing
  at timescales of mins, hours, days, …
Non-convex and hard to solve
  Huge literature since 1962
  Common practice: DC power flow (LP)
  Also: Newton-Raphson, interior point, …

## Slide 7: Optimal power flow (OPF)
Ian Hiskens, Michigan
OPF problem underlies numerous applications
nonlinearity of power flow equations  nonconvexity

## Slide 8
How to deal with nonconvexity
of power flows?
Two ideas
  exact semidefinite relaxation
Tutorial:
L, Convex relaxation of OPF, 2014
http://netlab.caltech.edu

## Slide 9
How to deal with nonconvexity
of power flows?
Two ideas
  exact semidefinite relaxation
  use grid as implicit power flow solver

## Slide 10: Key message
Large network of DERs
  Real-time optimization at scale
  Computational challenge: power flow solution
Online optimization [feedback control]
  Network computes power flow solutions in real time at scale for free
  Exploit it for our optimization/control
  Naturally adapts to evolving network conditions
Examples
  Slow timescale: OPF
  Fast timescale: frequency control

## Slide 11: Outline
Semidefinite relaxations of OPF
  Power flow models
  Offline algorithms
Online OPF
  Power flow models
Load-side frequency control
  Dynamic models
Zhao, Topcu, Li, L, TAC 2014
Tutorial:
L, Convex relaxation of OPF, 2014
http://netlab.caltech.edu

## Slide 12
Online OPF
Gan (FB)
Dvijotham (PNNL)
Tang

## Slide 13: Relaxations of OPF
But traditional algorithms are all offline …
… unsuitable for real-time optimization of
network of distributed energy resources

## Slide 14: Relaxations of OPF
We will compare our online algorithm to
relaxation wrt optimality and speed

## Slide 15: OPF
power flow equations
operational constraints
capacity limits
controllable
devices
uncontrollable
state

## Slide 16: OPF
power flow equations
operational constraints
capacity limits

## Slide 17: OPF
power flow equations
operational constraints
capacity limits

## Slide 18: OPF: eliminate y

## Slide 19: OPF: add barrier
L: nonconvex
add barrier function
to remove
operational constraints

## Slide 20: Online (feedback) perspective
control
x(t)
measurement,
communication
y(t)
physical
network
cyber
network

## Slide 21: Online gradient algorithm
gradient projection algorithm:
active control
law of physics
Explicitly exploits network as power flow solver
Naturally tracks changing network conditions

## Slide 22: Online gradient algorithm
gradient projection algorithm:
active control
law of physics
Results
Optimality
Tracking performance

## Slide 23: 1. Local optimality
Under appropriate assumptions
  x(t) converges to set of local optima
  if #local optima is finite, x(t) converges

## Slide 24: 1. Global optimality
Theorem
If co{local optima} are in A then
  x(t) converges to the set of global optima
  x(t) itself converges a global optimum if #local optima is finite

## Slide 25: 1. Global optimality
Theorem
  If SOCP is exact over X, then assumption holds

## Slide 26: 1. Suboptimality gap
  Informally, a local minimum is almost as good
  as any strictly interior feasible point
any local
optimum
any original
feasible pt
slightly away
from X boundary

## Slide 27: 2. Tracking performance
drifting
OPF
static
OPF

## Slide 28: 2. Tracking performance
Theorem
cost of Alg
optimal cost
dynamic
regret
rate of
drifting
subopt of
local min

## Slide 29: 2. Tracking performance
Theorem
cost of Alg
optimal cost
dynamic
regret
rate of
drifting
subopt of
local min

## Slide 30: 2. Tracking performance
cost of Alg
optimal cost
dynamic
regret
Theorem
  If rate of drifting is then per-step
is asymptotically bounded by
  Can made arbitrarily small at cost of computation
(local min)

## Slide 31: Simulations

## Slide 32
frequency control
Zhao, Topcu, Li, L, TAC 2014
http://netlab.caltech.edu
Mallada (JHU)
Li (Harvard)
Topcu (Austin)
Zhao (NREL)
Bialek (Skoltech)

## Slide 33: Motivation
2011 Southwest blackout
(1 min)
  All buses synchronized to same nominal frequency (US: 60 Hz; Europe/China: 50 Hz)
  Supply-demand imbalance  frequency fluctuation

## Slide 34: Why load-side participation
sec
min
5 min
60 min
primary
freq control
secondary freq control
economic
dispatch
Ubiquitous continuous load-side control can supplement generator-side control
  faster (no/low inertia)
  more reliable (large #)
  better localize disturbances
  reducing generator-side control capacity

## Slide 35: What is the potential
US:
operating reserve: 13% of peak
total GFA capacity: 18%
Lu & Hammerstrom (2006), PNNL
Residential load accounts
for ~1/3 of peak demand
61% residential appliances
are Grid Friendly

## Slide 36: How
How to design load-side frequency control ?
How does it interact with generator-side control ?

## Slide 37: Literature: load-side control
Original idea & early analytical work
  Schweppe et al 1980; Bergin, Hill, Qu, Dorsey, Wang, Varaiya …
Small scale trials around the world
  D.Hammerstrom et al 2007, UK Market Transform Programme 2008
Early simulation studies
  Trudnowski et al 2006, Lu and Hammerstrom 2006, Short et al 2007, Donnelly et al 2010, Brooks et al 2010, Callaway and I. A. Hiskens, 2011, Molina-Garcia et al 2011
Analytical work – load-side control
  Zhao et al (2012/2014), Mallada and Low (2014), Mallada et al (2014), Zhao and Low (2014), Zhao et al (2015)
  Simpson-Porco et al 2013, You and Chen 2014, Zhang and Papachristodoulou (2014), Ma et al (2014), Zhao, et al (2014),
Recent analysis – generator-side/microgrid control:
  Andreasson et al (2013), Zhang and Papachristodoulou (2013), Li et al (2014, 2016), Burger et al (2014), You and Chen (2014), Simpson-Porco et al (2013), Hill et al (2014), Dorfler et al (2014)

## Slide 38: Network model
generator or load
loads:
damping or uncontrollable
i : region/control area/balancing authority
branch power

## Slide 39: Network model
Generator bus: Mi > 0
Load bus: Mi = 0

## Slide 40: Network model
Generator bus: pi is real power injection
Load bus: pi is controllable load

## Slide 41: Generator-side control
generator bus:

## Slide 42: Load-side control
Load bus:
how to design feedback control ?

## Slide 43: Network model
Suppose the system is in steady state
Then: disturbance in gen/load …

## Slide 44: Load-side controller design
Control goals (while min disutility)
  Rebalance power & stabilize frequency
  Restore nominal frequency
  Restore scheduled inter-area flows
  Respect line limits
Zhao, Topcu, Li, Low
TAC 2014
Mallada, Zhao, Low
Allerton, 2014

## Slide 45: Load-side controller design
Control goals (while min disutility)
  Rebalance power & stabilize frequency
  Restore nominal frequency
  Restore scheduled inter-area flows
  Respect line limits
Zhao, Topcu, Li, Low
TAC 2014
Mallada, Zhao, Low
Allerton, 2014

## Slide 46: Load-side controller design
Design control law
whose equilibrium
solves:
power balance
inter-area flows
line limits
Control goals (while min disutility)
  Rebalance power & stabilize frequency
  Restore nominal frequency
  Restore scheduled inter-area flows
  Respect line limits
load disutility
freq will emerge as
Lagrange multiplier
for power imbalance

## Slide 47: Load-side controller design
Design control (G, F) s.t. closed-loop system
  is asymptotically stable
  has equilibrium that is optimal
power network
load control

## Slide 48: Load-side controller design
Idea: exploit system dynamic as part of primal-dual algorithm for modified opt
  Distributed algorithm
  Control goals in equilibrium
  Stability analysis
power network
load control

## Slide 49: Summary: control architecture
Primary load-side frequency control (linear PF)
completely decentralized
Theorem: globally stable dynamic, optimal equilibrium
Zhao, Topcu, Li, Low. TAC 2014
physical network

## Slide 50: Summary: control architecture
Mallada, Zhao, Low. Allerton 2014
Secondary load-side frequency control (linear PF)
communication with neighbors
Theorem: globally stable dynamic, optimal equilibrium
physical network
cyber network

## Slide 51: Summary: control architecture
With generator-side control, nonlinear power flow
load-side improves both transient & eq
Theorem: stable dynamic, optimal equilibrium
Zhao, Mallada, Low. CISS 2015
physical network
cyber network

## Slide 52: Simulations
Dynamic simulation of IEEE 39-bus system
Power System Toolbox (RPI)
Detailed generation model
Exciter model, power system
stabilizer model
Nonzero resistance lines

## Slide 53: Primary control

## Slide 54: Secondary control
Similar shape but local frequencies differ more, higher control effort, slightly longer settling time
Traditional AGC
Unified Control

## Slide 55: Secondary control
Unified Control enforces line limits
AGC blind to line limits
Traditional AGC
Unified Control

## Slide 56: Key message
Large network of DERs
  Real-time optimization at scale
  Computational challenge: power flow solution
Online optimization [feedback control]
  Network computes power flow solutions in real time at scale for free
  Exploit it for our optimization/control
  Naturally adapts to evolving network conditions
Examples
  Slow timescale: OPF
  Fast timescale: frequency control