## Slide 1: Optimal Storage Placement and Power Flow Solution
Stanford Nov 2016
Yujie Tang
Steven Low
Michael Chertkov
Krishnamurthy
Dvijotham
Notes: Power Flow Solution Methods
=========================
July 6, 2016: IEEE ACC Tutorial (Dan Molzahn)
Nov 3, 2016: Stanford Smart Grid Seminars (Ram Rajagopal, Chin-Woo Tan)
Optimal storage placement
=========================
Nov 3, 2016: Stanford Smart Grid Seminars (Ram Rajagopal, Chin-Woo Tan)

## Slide 2: Outline
Optimal storage placement
  Continuous network model
  Structural properties
Power flow solution
  Monotone operators
  contraction
  contraction
Dvijotham
Tang
Chertkov

## Slide 3: Motivation
Storage on distribution network
  Useful for renewable/DG integration
  CA mandates
    RPS: 33% by 2020, 50% by 2030
    3 IOUs to deploy 1.3GW battery by 2020
      At least ½ owned by IOUs
Design question: ideal deployment ?
  Where to place and how to size
  ... to minimize line loss
  ... assuming
    no other constraints such as real estate
    optimal charging/discharging operation

## Slide 4: Conclusion
Interested in design guidelines
  Structural properties of optimal solution
Placement and sizing
  (scaled) Monotone deployment is optimal
Charging/discharging schedule
  Always charge till full (when generation is highest)
  Always discharge till empty (when demand is highest)

## Slide 5: Continuous tree
[similar to Wang Turitsyn Chertkov (2012) ODE model of feeder line for power flow solution]
A continuous tree with underlying discrete tree
  Each segment (corresponding to a node in discrete tree) can be treated like a closed interval in R
  Order and integration are well defined on each segment

## Slide 6: Continuous power flow equations

## Slide 7: Continuous power flow equations
line loss
[ power flow equations: continuous version of Baran and Wu (1989) ]

## Slide 8: Linear approximation
Assumptions
loss is small relative to line flow
voltage magnitude ~ 1 pu
[ power flow equations: continuous version of Baran and Wu (1989) ]

## Slide 9: Linear approximation
Assumptions
loss is small relative to line flow
voltage magnitude ~ 1 pu
background injection:
common load shape in time
location-dependent scale & offset
[Smith, Wong, Rajagopal 2012]
charging rate

## Slide 10: Storage model
charging rate
SoC

## Slide 11: Optimal placement & sizing
energy loss
linear power
flow equation
state of charge
budget constraint
line flow

## Slide 12: Optimal placement & sizing
energy loss
linear power
flow equation
state of charge
budget constraint
background injection
charging
rate

## Slide 13: Optimal placement & sizing
energy loss
linear power
flow equation
state of charge
budget constraint

## Slide 14: Optimal placement & sizing
energy loss
linear power
flow equation
state of charge
budget constraint

## Slide 15: Outline
Optimal storage placement
  Continuous network model
  Structural properties
Power flow solution
  Monotone operators
  contraction
  contraction
Tang

## Slide 16: Linear network
[Tang and Low, CDC 2016]
compute:
given:
Theorem Optimal charging schedule
Follow load shape p(t) with an offset, or OFF
  Charge when injection is highest till full
  Discharge when injection is lowest till empty
charge
discharge
net injection is
flat (in time)

## Slide 17: Linear network
[Tang and Low, CDC 2016]
compute:
given:
Theorem Optimal charging schedule
Follow load shape p(t) with an offset, or OFF
  Charge when injection is highest till full
  Discharge when injection is lowest till empty
charge
discharge
flatten net injection

## Slide 18: Linear network
[Tang and Low, CDC 2016]
Theorem Optimal placement & sizing
Deploy most storage far away from substation
Decrease (scaled) storage capacity moving towards substation
... until running out of storage budget
Every node can have distributed generation (2-way power flow)
... as long as all nodes have same load shape (with different scales & offsets)

## Slide 19: Tree network
Theorem
Structural properties (roughly) extend to tree
optimal placement & sizing

## Slide 20: Tree network
Theorem
Structural properties (roughly) extend to tree
optimal schedule
charge
till full
discharge
till empty

## Slide 21: Simulations
IEEE 123-bus test system
More realistic model
Nonlinear DistFlow model
Different nodes have slightly different load shapes (from SCE)
Compare with optimal placement
Monotone property
Total loss
Optimal placement solved using SOCP relaxation of OPF
Notes: We first show that Theorem 3 holds when p(t) is allowed to have multiple maxima and minima. The load shape shown in Figure 4 is taken from Southern California Edison [19], which consists of load consumptions spanning a 72-hour period, and has multiple peaks and valleys. We employ its negative as p(t), and assume that at bus i, the background injection is given by ↵ip(t), where the scaling factor ↵i is the original load consumption of bus i from the IEEE 123 node test case. To make results clearer, we add a small amount of load to each bus that originally has no load consumption, so that ↵i > 0 and the scaled optimal capacities are well defined for all i. The amount of load added is 1/4 of the smallest original load consumption of a single bus.

## Slide 22: Simulations
Scaled monotone property roughly holds
Optimal placement & sizing from SOCP relaxation of OPF:
Notes: Optimal storage placement for the simplified IEEE 123 node test feeder with nonlinear DistFlow model when p ̃i(t) deviates from the common load shape. The radius of each colored solid circle is proportional to Bi⇤/↵i, and different colors correspond to different Btot.

## Slide 23: Simulations
Loss with assumptions (same load shape, linear PF) ~ optimal

## Slide 24: Tree network
Theorem
Structural properties (roughly) extend to tree
optimal placement & sizing

## Slide 25: Tree network
Theorem
Structural properties (roughly) extend to tree
optimal schedule
charge
till full
discharge
till empty

## Slide 26: Outline
Optimal storage placement
  Continuous network model
  Structural properties
Power flow solution
  Monotone operators
  contraction
  contraction
Dvijotham
Chertkov

## Slide 27: Power flow models
i
j
k
real & reactive power
conductance & susceptance
voltage
phasor
Given s, find V that satisfies

## Slide 28: Power flow models
i
j
k
real & reactive power
conductance & susceptance
voltage
phasor
Given (p,q), find (Vx, Vy) that satisfies

## Slide 29: Power flow models
i
j
k
real & reactive power
conductance & susceptance
voltage
phasor
In polar form (can be reparametrized into quadratic equations):

## Slide 30: Power flow solutions
Given s, find x that satisfies
where and is quadratic
Different power flow equations lead to different F
Different solution properties
Different computational efficiencies

## Slide 31: Power flow solutions
Given s, find x that satisfies
where and is quadratic
Let denote its Jacobian

## Slide 32: Power flow solutions
Classical algorithms
  Newton-Raphson, Gauss-Seidel, …
  Advantage: simple
  No guarantee: convergence, solution with desired properties, or all solutions
Homotopy-based algorithms
  Can find all PF solutions
  Computationally very expensive
Ours: compromise of 2 methods
  Characterize PF solution region with desirable properties (operation regime)
  Prove there is at most one solution in the region
  Fast computation to find the unique solution if exists or certify none exists in the region

## Slide 33: Outline
Introduction
Contractive operator method
  contraction
  contraction

## Slide 34: contraction
Let be nonempty, closed, convex, over which
is -strongly positive definite, i.e.
is -bounded, i.e.,
implying F is over D
-strongly monotone
-Lipschitz (because F is quadratic)

## Slide 35: contraction
Let be nonempty, closed, convex, over which
is -strongly positive definite, i.e.
is -bounded, i.e.,
implying F is over D
-strongly monotone
-Lipschitz (because F is quadratic)

## Slide 36: contraction
Theorem
  There is at most one PF solution in D
how to efficiently find it if exists, or certify otherwise ?
Let be nonempty, closed, convex, over which
is -strongly positive definite, i.e.
is -bounded, i.e.,

## Slide 37: contraction
Theorem
  is a contraction over with rate
  and a unique fixed point
  If then is the unique PF solution in D
  -approx solution can be computed in
  Otherwise, there is no PF solution in D
Consider
fixed point iterations

## Slide 38: contraction
Consider
Theorem
  is a contraction over with rate
  and a unique fixed point
  If then is the unique PF solution in D
  -approx solution can be computed in
  Otherwise, there is no PF solution in D
fixed point iterations

## Slide 39: contraction
Consider
Theorem
  is a contraction over with rate
  and a unique fixed point
  If then is the unique PF solution in D
  -approx solution can be computed in
  Otherwise, there is no PF solution in D
fixed point iterations

## Slide 40: Solution strategy
Consider
Application
  Let be desirable operation regime
  Compute s.t. and satisfies conditions 1 and 2 over
  Compute
  If fixed point then it is the unique desirable PF solution
  Otherwise, there is no PF solution in
voltage magnitudes
close to nominal values
line currents
lower than capacities

## Slide 41: Solution strategy
Consider
Application
  Let be desirable operation regime

## Slide 42: Solution strategy
Application
  Let be desirable operation regime
  Compute s.t. and satisfies conditions 1 and 2 over
  Compute
Consider

## Slide 43: Solution strategy
Application
  Let be desirable operation regime
  Compute s.t. and satisfies conditions 1 and 2 over
  Compute
  If fixed point and then it is the unique desirable PF solution
  Otherwise, there is no PF solution in
Consider

## Slide 44: Solution strategy
Consider
Application
  Let be desirable operation regime
  Compute s.t. and satisfies conditions 1 and 2 over
  Compute
  If fixed point and then it is the unique desirable PF solution
  Otherwise, there is no PF solution in

## Slide 45: Solution strategy
Consider
Application
  Let be desirable operation regime
  Compute s.t. and satisfies conditions 1 and 2 over
  Compute
  If fixed point and then it is the unique desirable PF solution
  Otherwise, there is no PF solution in

## Slide 46: Enhancement through scaling
Instead of solving
solve, for invertible ,
Maximize monotonicity region by choice of
Optimal W* yields largest monotonicity region

## Slide 47: Outline
Introduction
Contractive operator method
  contraction
  contraction

## Slide 48: contraction
Let . Suppose, over ,
is row -diagonally dominant, i.e.
is -bounded, i.e.,
Consider

## Slide 49: contraction
Let . Suppose, over ,
is row -diagonally dominant, i.e.
is -bounded, i.e.,
Consider

## Slide 50: contraction
Let . Suppose, over ,
is row -diagonally dominant, i.e.
is -bounded, i.e.,
Consider

## Slide 51: contraction
Consider
Theorem
  is a contraction over with rate
  and a unique fixed point
  If then is the unique PF solution in D
  Otherwise, there is no PF solution in D
Theorem suggests a similar solution strategy

## Slide 52: Performance
monotone op method succeeds when Newton-Raphson fails
IEEE 14-bus network
IEEE 39-bus network

## Slide 53: Conclusion
PF solution through contraction
  Characterize PF solution region with desirable properties
  Prove there is at most one solution in the region
  Fixed-point iteration computes efficiently…
  … either finds the unique solution or certifies none exists in the region