## Slide 1: Adaptive Charging Network for electric vehicles
March 2017
Steven Low
George Lee
Notes: PowerFlex is a Caltech startup co-founded by George Lee and Steven Low
Dec 9, 2016: GlobalSIP, Washington DC (invited Meng Wang)
March 30, 2017 NSF: Barbara Kenny, Prakash Balan AIR PM, Arlington, VA

## Slide 2: ACN testbed
Z. Low, Cornell
T. Lee, CIT
C. Ortega, CIT
K. Erliksson, Lund
Z. Lee, CIT
D. Chang, CIT
R. Lee, CIT

## Slide 3: ACN theory
L. Chen, CIT
L. Chen, Colorado
Y. Nakhira, CIT
D. Guo, CIT

## Slide 4: Electricity gen & transportation
They consume the most energy
  Consumer 2/3 of all energy in US
They emit the most greenhouse gases
  Emit >1/2 of all greenhouse gases in US
To drastically reduce greenhouse gases
  Increase renewable generations
  Electrify transportation

## Slide 5: EV & charging
CA 2025 goal
  1.5 million zero emission cars
Accelerating growth
  2011-2013: EVs have grown by 8x in US
  2011-2013: #Public charging stations grown by 7x in US
Painpoints
  Overcrowding, EV shuffling
source:
Chargepoint
1st week reservation:
325K, $14B
Tesla Model 3 (4/2016)

## Slide 6: Publications
Adaptive Charging Network for Electric Vehicles. Dec 2016
George Lee, Ted Lee, Zhi Low, Steven H. Low and Christine
Ortega, IEEE GlobalSIP, Washington, DC
Smoothed Least-laxity-first Algorithm for EV Charging. May 2017. Y. Nakahira, N. Chen, L. Chen and S. H. Low.
Proc ACM e-Energy Conference, Hong Kong
Optimal Online Adaptive Electric Vehicle Charging. July 2017
Linqi Guo, Karl F. Erliksson and Steven H. Low.
Proc. IEEE PES General Meeting, Chicago, IL
The National Electric Transportation Infrastructure Working Council (IWC) Meeting, San Francisco, CA, November 2016

## Slide 7: Outline
Theory and algorithms
  Algorithm design
  Simulations and analysis
ACN testbed
  System design
  Caltech pilot

## Slide 8: Charging model
energy
demand
(miles / kWh)
arrival /
departure
time
peak
charging
rate (kW)

## Slide 9: Charging model

## Slide 10: Offline optimal charging
Offline optimal problem is a linear program
charge only after ai before di
not exceeding peak rate

## Slide 11: Offline optimal charging
Offline optimal problem is a linear program
meet energy demand
not exceed limit;
can generalize to
linear constraints

## Slide 12: Online LP
Offline LP is not implementable
  It needs future EV information
Implement Online LP
  Solve LP with current EVs, assuming no future arrival
  Update remaining energy demand after each online LP iteration
  Model-predictive control

## Slide 13: Performance: online LP
Suppose cost coefficients are uniformly monotone
Theorem
If online LP is feasible, then it attains offline optimal
Guo, Erliksson, L. PES GM 2017

## Slide 14: Performance: online LP
Theorem
competitive ratio can be arbitrarily bad
Guo, Erliksson, L. PES GM 2017

## Slide 15: Performance: online LP
feasibility of online LP
~ feasibility of offline LP
(averaged over all locations
and all days for each dataset)
normalized difference
normalized difference

## Slide 16: Performance
peak demand reduction
Caltech data (Feb – May, 2016)
savings = infrastructure, demand charge
data: g2016mtv2000
data: CAgarage2016

## Slide 17
Karl Erliksson 2016 SURF
Conclusions
savings increase in initial laxity
significant savings even at low laxity
Daily peak power | Uncontrolled charging | ACN | Power savings
Caltech | 85.3 kW | 33.8 kW | 60%
Mountain View | 46.2 kW | 28.4 kW | 34%
Sunnyvale | 94.0 kW | 56.2 kW | 29%
Adaptive charging network
savings = infrastructure, demand charge
Notes: The transformer capacity is 7.2 kW (25 kW shared between 4 houses). Each car can charge at a peak rate of 7.2 kW. Therefore all three cars charging at their peak rate will exceed the transformer limit.
The demo will run over 11 minutes with the following scenario:
Three cars will be plugged in at different times with different energy demands and departure times:
  Car 1: arrives at time 0, departs at time 11 mins, needs 0.71 kWh.
  Car 2: arrives at time 2 mins, departs at 5 mins, needs 0.36 kWh.
  Car 3: arrives at time 3 mins, departs at 8 mins, needs 0.25 kWh.
The scenario is designed to illustrate the importance of smart charging (and other system functions; see below):
  Dumb charging where each car charges at its peak will exceed transformer limit.
  Static sharing policy will not satisfy EV energy demands.
  Only dynamic adaptation based on real-time information can work, as shown in the diagram below.

## Slide 18
Data cleaning
Remaining #EVs (charging sessions)
Mountain View: 44,587
Sunnyvale: 6,466
CA Garage: 1,309
Total: 52,362 sessions, in 2016 (over a few months)
104 locations
>4,000 charging days
Notes: The transformer capacity is 7.2 kW (25 kW shared between 4 houses). Each car can charge at a peak rate of 7.2 kW. Therefore all three cars charging at their peak rate will exceed the transformer limit.
The demo will run over 11 minutes with the following scenario:
Three cars will be plugged in at different times with different energy demands and departure times:
  Car 1: arrives at time 0, departs at time 11 mins, needs 0.71 kWh.
  Car 2: arrives at time 2 mins, departs at 5 mins, needs 0.36 kWh.
  Car 3: arrives at time 3 mins, departs at 8 mins, needs 0.25 kWh.
The scenario is designed to illustrate the importance of smart charging (and other system functions; see below):
  Dumb charging where each car charges at its peak will exceed transformer limit.
  Static sharing policy will not satisfy EV energy demands.
  Only dynamic adaptation based on real-time information can work, as shown in the diagram below.

## Slide 19: Smoothed Least laxity first (sLLF)
energy
demand
(miles / kWh)
arrival /
departure
time
peak
charging
rate (kW)
no look-ahead

## Slide 20: Smoothed Least laxity first (sLLF)
energy
demand
(miles / kWh)
arrival /
departure
time
peak
charging
rate (kW)
remaining
time
minimum
required

## Slide 21: Smoothed Least laxity first (sLLF)
Algorithm: max min laxity at next time
Nakahira, et al, e-Energy 2017

## Slide 22: Smoothed Least laxity first (sLLF)
 water-filling algorithm
Theorem
sLLF rates solves
Nakahira, et al, e-Energy 2017

## Slide 23: Smoothed Least laxity first (sLLF)
Theorem
sLLF rates are
Proportionally fair
Maxmin fair
Nakahira, et al, e-Energy 2017

## Slide 24: Smoothed Least laxity first (sLLF)
Nakahira, et al, e-Energy 2017

## Slide 25: Outline
Theory and algorithms
  Algorithm design
  Simulations and analysis
ACN testbed
  System design
  Caltech pilot

## Slide 26
garage loads
(lighting, fans, etc)
EV switch
panel
EV switch
panel
480V
800A
utility
company
Caltech
substation
480V
225A
208V
500A
…
150 kVA EV
3-phase
transformer
…
charger
208V
80A
Caltech
ACN
main switch
panel
Overall system

## Slide 27
Adaptive charging network
chargers
150kVA transformers
First pilot @Caltech garage
  50+ adaptive Level 2 chargers
  2x 150kVA transformers
  Operational since Feb 2016
main panel
debugging

## Slide 28
(60 chargers; since 2/2016; 400K+ miles delivered, 140+ tons of GHG avoided; 3/2017)
Caltech ACN
  Provide target charging capacity at much lower infrastructure & operating costs (30% - 60% savings)
  Provide ancillary energy services

## Slide 29
Hardware design
network
cloud

## Slide 30
database
servers
facility
operator
utilities
ISO
mobile
app
learning &
prediction
station &
subscription mgt
alerts &
visualization
wireless & wireline network
OpenADR
2.0
OpenADR 2.0
communication & interfaces
control &
optimization
(LMC)
Software design

## Slide 31: Indoor or outdoor

## Slide 32: Adaptation
PV
charging rate
(EVSE)
Fair sharing, Aug 2016
Real-time adaptation
DR capability, Oct 2016
Capability to track PV
generation in real time
JPL demo
30A
24A
16A
8A

## Slide 33: Management interface
Real-time monitoring
Deployed on ACN cloud server

## Slide 34: Key benefits
Provide target charging capacity at 30%-60% lower costs
  infrastructure costs
  operating costs (demand charges)
Flexibility in implementing operator objectives
  min electricity bill
  min charging time
  max asset utilization
  max system robustness
Potential for providing DR/ancillary services
  Help distribution grid operation

## Slide 35
. . .
distribution
grid
transmission
grid
PF cloud
ACN input
utility input
ISO input
utilities
ISO markets
driver
input
ACN
PF cloud
input
driver
input
ACN
PF cloud
input

## Slide 36: Simulation tool
Karl Erliksson 2016 SURF
Notes: 9:40

## Slide 37: Backup Slides
Notes: PowerFlex is a Caltech startup co-founded by George Lee and Steven Low
Dec 9, 2016: GlobalSIP, Washington DC (invited Meng Wang)

## Slide 38
data: CAgarage2016
Daily peak power
without adaption
Daily peak power
with adaptation
ACN benefit
Caltech data (Feb – May, 2016)
savings = infrastructure, demand charge
Notes: The transformer capacity is 7.2 kW (25 kW shared between 4 houses). Each car can charge at a peak rate of 7.2 kW. Therefore all three cars charging at their peak rate will exceed the transformer limit.
The demo will run over 11 minutes with the following scenario:
Three cars will be plugged in at different times with different energy demands and departure times:
  Car 1: arrives at time 0, departs at time 11 mins, needs 0.71 kWh.
  Car 2: arrives at time 2 mins, departs at 5 mins, needs 0.36 kWh.
  Car 3: arrives at time 3 mins, departs at 8 mins, needs 0.25 kWh.
The scenario is designed to illustrate the importance of smart charging (and other system functions; see below):
  Dumb charging where each car charges at its peak will exceed transformer limit.
  Static sharing policy will not satisfy EV energy demands.
  Only dynamic adaptation based on real-time information can work, as shown in the diagram below.